## Slide 1
POWERGUARD
Electricity Theft Detection System
Complete Deep Dive Study Guide
8
Detection Factors
5
ML Models
47+
Engineered Features
4
Micro- services
ML + Heuristic Hybrid | SGCC Dataset | Ensemble Strategy | SHAP Explainability

## Slide 2
THE PROBLEM: Electricity Theft
Non-Technical Loss (NTL)
India loses ~Rs.1.5 lakh crore/year to theft
Globally: $96 billion problem
20-25% of total electricity generated is stolen
Why Can't Humans Find It?
Manual inspection covers only 2-5% of meters/year
Skilled thieves make it visually undetectable
Inspections cost Rs.500-2000 per visit
Data spoofing leaves zero physical evidence
Our Solution
Use smart meter telemetry data (already being collected)
6 dimensions: consumption, voltage, current, power factor, frequency, tamper
ML + rule-based heuristics to find anomalies
Explainable results operators can act on
Technical Loss vs NTL
Technical: Heat in wires (physics, predictable)
Non-Technical: Theft (anomalous patterns, ML detectable)

## Slide 3
THE 6 INPUT DIMENSIONS
1. Consumption
Unit: kWh
Normal: 0.5-20
How much electricity consumed
2. Voltage
Unit: Volts
Normal: 190-250V
Electrical pressure in line
3. Current
Unit: Amps
Normal: 0.5-30A
Flow of electrons through meter
4. Power Factor
Unit: 0-1
Normal: 0.85-1.0
Real/Apparent power ratio
5. Frequency
Unit: Hz
Normal: 49.5-50.5
Grid oscillation rate
6. Tamper Flag
Unit: Bool
Normal: false
Hardware sensor trigger
Different theft techniques disturb different dimensions -- that's why we analyze all 6 together

## Slide 4
THE 8 DETECTION FACTORS (Overview)
Consumption Drop [25%]
Meter bypass during daytime
Tamper Detection [20%]
Physical hardware tampering
Current Anomaly [15%]
Current shunted around meter
Voltage Anomaly [10%]
Voltage manipulation
Power Factor [10%]
Load manipulation via capacitors
Pattern Irregularity [10%]
Day/night inversion, chaos
Frequency Deviation [5%]
Illegal grid tapping
Flat-line Detection [5%]
Spoofed/replayed data
Each factor scores 0.0 (clean) to 1.0 (theft). Combined via weighted average + boosting logic.

## Slide 5
FACTOR 1: CONSUMPTION DROP [Weight: 25%]
What it detects:
Meter bypass during daytime hours
The Physics / Logic:
Zero kWh during 8AM-8PM is impossible
People use ACs, fridges, lights during day
Zero during peak hours = bypassed meter
Also checks: avg < 30% of baseline
Algorithm:
Filter to peak hours (8AM-8PM)
Count zero-kWh readings
Score = min(1.0, (zeros/total) x 5)
If avg < 30% baseline -> floor at 0.7
x5 multiplier: 20% zeros = score 1.0
Why 25% weight?
Strongest single indicator. Appears in 70%+ of confirmed theft cases.

## Slide 6
FACTOR 2: CURRENT ANOMALY [Weight: 15%]
What it detects:
Physical meter bypass (current shunted around meter)
The Physics / Logic:
Ohm's Law: P = V x I
If voltage=220V, current=0.05A, but consumption>0
-> Physically IMPOSSIBLE without bypass
Current must flow through bypass wire
Algorithm:
Find: current<0.1A AND voltage>200V
AND consumption>0
Score = min(1.0, (count/total) x 4)
Zero current + consumption>0.5 -> x8 boost
Violates basic electrical physics
Why 15% weight?
Physics-based signal. Very hard to fake or explain away. Less common than consumption drops.

## Slide 7
FACTOR 3: TAMPER DETECTION [Weight: 20%]
What it detects:
Physical tampering with meter hardware
The Physics / Logic:
Smart meters have accelerometers,
reed switches, case-open detectors
Physical opening/shaking/magnet -> tamper flag
Consecutive flags = sustained tampering
Random faults are isolated (1-2 flags)
Algorithm:
Score = min(1.0, tamper_ratio x 10)
-> 10% tamper rate = score 1.0
Consecutive check:
5+ consecutive flags -> score 0.9
(deliberate, not random noise)
Why 20% weight?
Physical hardware signal. Very reliable but can have false positives (storms, accidents).

## Slide 8
FACTOR 4: VOLTAGE ANOMALY [Weight: 10%]
What it detects:
Voltage manipulation to reduce metered consumption
The Physics / Logic:
Thieves use 'voltage divider' devices
Energy = V x I x t
Lower voltage = lower recorded consumption
Safe band: 190V-250V (India standard)
Extreme (<170V or >270V) = deliberate
Algorithm:
Count readings outside 190-250V
Score = min(1.0, (outliers/total) x 3)
Extreme voltage (<170V or >270V):
5x multiplier (deliberate manipulation)
vs grid fluctuation
Why 10% weight?
Voltage issues CAN be legitimate (grid problems during monsoon). Weighted lower for this reason.

## Slide 9
FACTOR 5: POWER FACTOR [Weight: 10%]
What it detects:
Load manipulation using capacitor banks
The Physics / Logic:
PF = Real Power / Apparent Power
PF=1.0: perfect efficiency
PF=0.3: 70% energy wasted as reactive
Thieves use capacitors to create low PF
Meter records less 'real power'
Algorithm:
Count readings where PF < 0.5
Score = min(1.0, (low_pf/total) x 3)
Cross-reference:
PF<0.3 AND consumption<20% baseline
-> x5 multiplier (VERY strong signal)
Why 10% weight?
Low PF alone can be legitimate (old motors). Combined with low consumption = strong theft signal.

## Slide 10
FACTOR 6: PATTERN IRREGULARITY [Weight: 10%]
What it detects:
Reversed, chaotic, or artificially manipulated patterns
The Physics / Logic:
Normal: peaks at 8AM and 7PM
Theft: HIGH at 2AM, ZERO during day
Stealing when inspectors aren't watching
Also detects erratic/random patterns
Algorithm:
CV = std / mean
Score = min(1.0, (CV-0.5) / 1.5)
Day/Night Inversion:
night_avg > 2x day_avg -> 0.6
day=0 but night>0 -> 0.85
mean=0 (active meter) -> 0.8
Why 10% weight?
Catches behavioral anomalies that physics-based measures miss.

## Slide 11
FACTOR 7: FREQUENCY DEVIATION [Weight: 5%]
What it detects:
Grid-level anomalies from illegal high-power tapping
The Physics / Logic:
India grid: exactly 50 Hz (+/- 0.5 Hz)
Most tightly controlled grid parameter
Deviations: large illegal loads tapping in
Or generator running unsynchronized
Algorithm:
Normal band: 49.0 - 51.0 Hz
Count readings outside band
Score = min(1.0, (outliers/total) x 4)
Weak individual signal
Useful in combination with others
Why 5% weight?
Frequency affects entire grid, not just one meter. Weakest individual signal but adds value in ensemble.

## Slide 12
FACTOR 8: FLAT-LINE DETECTION [Weight: 5%]
What it detects:
Spoofed/replayed meter data (hacked firmware)
The Physics / Logic:
Real consumption is NEVER perfectly constant
Even a fridge has compressor cycles
Same kWh for 24 hours = pre-recorded fake data
Very specific attack (firmware hacking)
Algorithm:
unique_ratio = unique_values / total
Score = min(1.0, (1-unique_ratio)x2 - 0.5)
Last-24 check:
<= 2 unique values in 24 readings
-> score floor at 0.9
Why 5% weight?
Very specific attack type. When present, extremely obvious. But rare (requires technical sophistication).

## Slide 13
WEIGHTED SCORING & BOOSTING LOGIC
The Formula:
theft_prob = (drop x 0.25) + (tamper x 0.20) + (current x 0.15) + (voltage x 0.10)
+ (PF x 0.10) + (pattern x 0.10) + (freq x 0.05) + (flatline x 0.05)
Boost Rule 1: Multi-Measure Agreement
If 3+ factors score above 0.5:
theft_prob = min(1.0, theft_prob x 1.3)
Why? Multiple independent detectors agreeing means real probability is HIGHER than weighted average.
Boost Rule 2: High-Confidence Floor
If ANY factor >= 0.9:
theft_prob = max(0.40, theft_prob)
Why? One factor screaming 'theft' at 0.9 should NEVER be washed out by 7 clean factors.
Decision Threshold: anomaly_flag = true if probability >= 30%
Why 30% (not 50%)? Missing a thief costs Rs.50,000+/year. A false alarm costs Rs.500 (one inspection). 100:1 cost ratio.

## Slide 14
WORKED EXAMPLE: Scoring a Suspicious Meter
Factor Scores:
Consumption Drop: 0.80 x 0.25 = 0.200
Tamper Detection: 0.90 x 0.20 = 0.180
Current Anomaly: 0.70 x 0.15 = 0.105
Voltage Anomaly: 0.30 x 0.10 = 0.030
Power Factor: 0.20 x 0.10 = 0.020
Pattern Irregular: 0.40 x 0.10 = 0.040
Frequency Deviat: 0.10 x 0.05 = 0.005
Flat-line: 0.00 x 0.05 = 0.000
Weighted Sum = 0.580 (58%)
Boost Rule 1: 3 factors > 0.5 (drop, tamper, current) -> x1.3
0.580 x 1.3 = 0.754 (75.4%)
Result: 75.4% -> CRITICAL RISK -> Immediate field investigation

## Slide 15
FEATURE ENGINEERING: 47+ Features in 6 Categories
Statistical (14)
mean, std, CV, skewness, kurtosis, percentiles (p10/25/75/90), IQR, range, min, max, median
Temporal (10)
weekday/weekend ratio, seasonal Q1-Q4, month-over-month changes, trend ratio, autocorrelation (lag-1, lag-7)
Anomaly (9)
zero-day count/ratio, sudden drops, flatline days, unique ratio, volatility index, below-baseline ratio
Comparative (3)
zone z-score deviation, zone percentile rank, ratio-to-zone average
Metadata (6)
consumer type (one-hot x3), baseline kWh, sanctioned load, consumption-to-sanctioned ratio
Advanced (5)
entropy, last/first 30-day ratio, max consecutive below-threshold, weekday/weekend means
Raw '10 kWh today' is not enough. ML models need rich, multi-dimensional feature views.

## Slide 16
CLASS IMBALANCE: 91.5% Honest vs 8.5% Theft
The Problem: Accuracy Paradox
A model that ALWAYS predicts 'Honest' gets 91.5% accuracy but catches ZERO thieves. Useless!
Solution 1: SMOTE
Creates synthetic thief samples Math: x_new = x_i + lambda x (x_zi - x_i) Balances to 50/50 training set
Solution 2: Class Weights
Model penalizes missing thief 6.25x more weight = n_total / (2 x n_theft) Forces model to 'care about' thieves
Solution 3: Threshold Tuning
Find threshold that maximizes F1-score Usually ~0.35-0.45 (not default 0.50) Lower = catch more thieves

## Slide 17
THE 5 ML MODELS
Random Forest
300 trees voting max_depth=20, class_weight=balanced Strength: Feature importance
XGBoost
300 sequential boosted trees L1/L2 regularization, scale_pos_weight Strength: Best for tabular data
DNN
128->64->32 neural network Dropout 40%, BatchNorm, Early Stop Strength: Non-linear patterns
LSTM
2 stacked layers (128->64) Memory gates, dropout 0.3 Strength: Time-series sequences
Isolation Forest
200 trees, unsupervised No labels needed, contamination=0.1 Strength: Catches novel theft

## Slide 18
ENSEMBLE STRATEGY: Combining 5 Models
Soft Voting (Simple Average)
P_ensemble = (P_RF + P_XGB + P_DNN + P_LSTM + P_ISO) / 5
Example:
RF: 0.72 XGB: 0.68 DNN: 0.81
LSTM: 0.55 ISO: 0.60
Ensemble = 0.672 (67.2%)
Stacking (Meta-Learner)
Logistic Regression learns optimal weights for each model's prediction:
P = sigmoid(w1*P_RF + w2*P_XGB + w3*P_DNN + w4*P_LSTM + w5*P_ISO + b)
If XGBoost is consistently more reliable, meta-learner automatically gives it higher weight.
Why Not Just Use the Best Model?
Every model has blind spots. RF can't capture complex interactions. XGBoost may overfit. DNN is a black box. LSTM is overkill for non-temporal patterns. Isolation Forest has false positives.
The ensemble lets models COVER for each other's weaknesses.

## Slide 19
EXPLAINABILITY: SHAP + Heuristic Breakdown
The Black-Box Problem: Inspector asks "WHY 90% theft?" -- "Because neural network said so" is NOT acceptable.
Solution 1: SHAP Values
Game-theory math (Shapley values) breaks down which feature caused the high score:
anom_zero_day_ratio: +0.23 (UP)
stat_cv: +0.18 (UP)
comp_zone_deviation: +0.15 (UP)
meta_baseline_kwh: -0.05 (down)
Solution 2: 8-Measure Breakdown
The heuristic ALWAYS runs to provide visual breakdown on dashboard:
Consumption Drop: 80%
Tamper Detection: 90%
Current Anomaly: 70%
Voltage Anomaly: 30%
Power Factor: 20%
Physical explanation operators can understand and act on.

## Slide 20
TRAINING PIPELINE: 7 Phases
Phase 1: Load SGCC Dataset
42,372 consumers x 1,035 days 91.5% honest / 8.5% theft
Phase 2: Preprocessing
Forward/backward fill missing values Winsorize at 5th/95th percentile Engineer 47-65 features
Phase 3: Class Imbalance
SMOTE (k=5 neighbors) Cost-sensitive class weights
Phase 4: Train 5 Models
RF(300) + XGBoost(300) + DNN + LSTM + Isolation Forest
Phase 5: Ensemble
Soft Voting + Stacking Optimal threshold tuning
Phase 6: Evaluation
Accuracy, Precision, Recall, F1 AUC-ROC, PR-AUC, 5-Fold CV
Phase 7: SHAP
TreeExplainer on Random Forest Top 15 features by importance

## Slide 21
6 SYNTHETIC THEFT SCENARIOS
1. Meter Tampering
Consumption x 0.1-0.4 Adjusted calibration
2. Bypass
Zero consumption blocks Copper wire around CT
3. Billing Irregularity
30-70% readings replaced Bribed reader / hacked billing
4. Unauthorized Tap
Sudden drop to near-zero Direct grid connection
5. Flat-line Spoof
Constant value forever Hacked meter firmware
6. Gradual Decay
Exponential decay to 5% Deliberate mechanical degradation
Each starts at random point (20-80% through timeline), maintains realistic seasonality before theft

## Slide 22
EVALUATION METRICS
Precision
TP / (TP+FP)
Of all 'theft' predictions, how many correct?
Recall
TP / (TP+FN)
Of all actual thieves, how many caught?
F1-Score
2*(P*R)/(P+R)
Harmonic mean of Precision & Recall
AUC-ROC
Area under curve
Discrimination ability across all thresholds
Confusion Matrix & 5-Fold Cross-Validation
TN (True Negative) = Honest correctly identified
TP (True Positive) = Thief correctly caught!
FP (False Positive) = False alarm (wasted inspection, cost: Rs.500)
FN (False Negative) = MISSED thief! (cost: Rs.50,000+/year)
5-Fold Stratified CV: Split data into 5 parts, train on 4, test on 1. Rotate 5 times. Report mean +/- std.

## Slide 23
SYSTEM ARCHITECTURE: 4 Microservices
React Frontend
Vite, Dashboard, Port 5173 7 pages + JWT auth Recharts visualization
Node.js API
Express, Port 5000 Auth, CRUD, Stats Orchestrates ML calls
FastAPI ML Service
Python, Port 8000 8-Measure Heuristic Ensemble Model
MongoDB
Port 27017 Meters, Readings, Alerts Compound Indexes
Frontend --(REST/JSON)--> Backend --(HTTP POST)--> ML Service | Backend --(Mongoose)--> MongoDB
Triple-Layer Fallback (System NEVER Fails)
Layer 1: ML Ensemble (ensemble_model.pkl) -> Highest accuracy
Layer 2: Python Heuristic (8-measure rules) -> No model file needed
Layer 3: JavaScript Fallback (same algorithm in JS) -> Zero external dependencies
Availability > DRY principle for critical infrastructure

## Slide 24
RISK CLASSIFICATION: 4 Tiers
LOW
0% - 29%
No action needed
MEDIUM
30% - 49%
Inspect within 30 days
HIGH
50% - 74%
Inspect within 7 days
CRITICAL
75% - 100%
Immediate investigation
Data Flow: Button Click to Result
1. User clicks 'Analyze Anomalies' on a meter
2. Frontend sends POST /api/analyze/:meterId (JWT attached)
3. Backend verifies ownership, fetches 30 days of readings (~720 hourly)
4. Backend computes stats (mean/std/min/max for all 6 dimensions)
5. Backend POSTs to ML Service with 15s timeout
6. ML Service runs ensemble (or heuristic fallback), returns 8 scores
7. If anomaly -> Alert created in MongoDB -> Red banner + 8 progress bars

## Slide 25
SUMMARY
What We Built:
PowerGuard: full-stack ML-powered electricity theft detection system
Analyzes 6-dimensional smart meter telemetry in real-time
8-measure weighted heuristic engine with per-factor explainability
5-model ML ensemble (RF + XGBoost + DNN + LSTM + Isolation Forest)
Trained on SGCC dataset (42,372 consumers) with SMOTE for class imbalance
47+ engineered features across 6 categories
SHAP explainability for transparent, actionable predictions
4-service microservice architecture (React + Node.js + FastAPI + MongoDB)
Triple-layer fallback ensuring zero downtime
4-tier risk classification with one-click bulk analysis
For every component: What? -> Why? -> How? -> Alternatives? -> Trade-offs? -> What would I change?